## Slide 1
Reducing Shock Interactions in a High Pressure Turbine via 3D Aerodynamic Shaping
Braden Hancock
Brigham Young University
B.S. Mechanical Engineering
Graduation 2014
Mentor: Dr. John Clark, AIAA “Engineer of the Year” 2012

## Slide 2
Motivation
Failed engine of an Airbus A380-800
As shown by NY Times , 4 Nov 2010
The result of High Cycle Fatigue (HCF) failure in a gas turbine engine

## Slide 3
Outline
Causes of HCF Failure
Method of 3D Aerodynamic Shaping
  Experimental Results - Benchmark
Method of Surface Normal Projections (SNP)
  Experimental Results - Comparison
Conclusions

## Slide 4
Shock Reflections
Unsteady interactions in a high pressure contra-rotating turbine:
1) Unsteady shock/boundary-layer interaction
2) Shock/shear-layer interactions
3) Moving shock/boundary-layer interaction
4) Reflected shocks
5) Shock/shock interaction
“A decrease in the level of empiricism in [unsteady flows] would be of significant value in the engine development process…”
-Greitzer, E. M., Tan, C. S., Wisler, D. C., Adamczyk, J. J., and Strazisar, A. J., 1994. “Unsteady Flows in Turbomachines: Where’s the Beef?,” Unsteady Flows in Aeropropulsion, ASME AD-Vol. 40, pp. 1-11.
Rotation
oblique shock
reflection surface
reflected shock
location
blade
vane
blade
blade
vane

## Slide 5
Shock Reflection Movement
Direction of Travel
Velocity
of Medium
Shock Wave
Velocity
of Medium
Reflected Shock Wave

## Slide 6
Direction of Travel
Velocity
Velocity
Shock Reflection Movement
Shock Wave
Reflected Shock Wave

## Slide 7
3D Aerodynamic Shaping
Baseline
Reverse-Bowed
Bowed
0
5
100 DFT mag. / Pt inlet
Upstream vanes
Resulting pressure distributions on upstream blades
Root
Tip

## Slide 8
Axial
Engine Orientation
Radial
Circumferential

## Slide 9
3D Aerodynamic Shaping
Baseline
Reverse-Bowed
Bowed
0
5
100 DFT mag. / Pt inlet
Upstream vanes
Resulting pressure distributions on upstream blades
Root
Tip

## Slide 10
Genetic Algorithm
Initial Generation
Calculate Fitness
Selection
Mating
Mutation
New Generation
Many chromosomes together describe an individual
.01742
.92645
…017423508192645…
Two successful individuals mate to form new individuals
…016354071287324…
… 0 1 7 4 2 3 5 0 8 1 9 2 6 4 5 …
…017423508187324…
…016354071292645…
Random mutation occurs occasionally
…017423508192645…
…017473508192645…

## Slide 11
3D Unsteady RANS Analysis
fitness
SP
ΔΦ
P ′loc
Genetic Algorithm (GA) Data | 
Number of Processors | 96
Generations | 16
Population size | 24
Hours of Runtime per Generation | 23.3
Fitness Criteria
Proximity of high pressure point to the root
How spread out in time the peak pressures are
Prevent unsteadiness in the trouble spot

## Slide 12
Results of CFD Analysis
-180⁰
180⁰
100 DFT mag. / Pt inlet , Phase Angle
Baseline
Bowed
0
5
100 DFT mag. / Pt inlet
The distribution of:
a) total static pressure in terms of DFT magnitude
b) phase angle in degrees
on the blade suction side due to the baseline and optimized vanes:
Pressure
Phase Angle
Baseline
Bowed
a)
b)

## Slide 13
Surface Normal Projections (SNP)
Standard Vane
Bowed Vane
Shock reflections plotted from the pressure side of a downstream vane to the suction side of an upstream blade

## Slide 14
Additional Considerations
Standard
The relative magnitudes of shock reflections on an upstream blade from a downstream vane
Bowed
An example of the blockage that can occur due to the presence of an adjacent vane in the line of sight of the projecting surface.
root
tip

## Slide 15
Genetic Algorithm Optimization
Genetic Algorithm Comparison |  | 
 | CFD Approach | SNP Approach
Population size | 24 | 48
Generations | 16 | 80
Pitch Change Range | 0 - 20 | (-100) - 100
Computation Time per Individual | 84000 s | 6 s
(1)
(2)
Nomenclature
center of reflection (by span %)
radial distance of vertex i from root
magnitude of reflection at vertex i
Total magnitude of reflections
fitness
(3)
Equations

## Slide 16
Fitness Trends

## Slide 17
Center of Reflection

## Slide 18
Relative Magnitude of Reflection

## Slide 19
Results of Projection Calculations
Baseline
CFD Optimal
Normal Projection Optimal
0
5
100 DFT mag. / Pt inlet
48% span
29% span
6% span
100% span
0% span
M = 1.00
M = 0.01
total sum of reflections
M 1.00

## Slide 20
What’s Next?
New transonic cascade facility is on-line (2D)
Annular-Cascade, HPT Stage, and Stage +1/2 Testing in the Turbine Research Facility (3D)

## Slide 21
Conclusions
1) Vane bowing has been shown to be a viable method for redirecting shock waves to regions of the blade where their detrimental effects will be mitigated.
2) Surface normal projections from downstream vanes may be used to estimate the results of shock reflections on upstream blades.
Reduction of pressure fluctuations by 2 orders of magnitude
  Translation of center of reflection by 42% span
3) Including the SNP method in the design of turbine airfoils holds significant advantages over an approach consisting exclusively of CFD simulations.
Reduction of computational time per airfoil by 4 orders of magnitude
Baseline
48% span
6% span
Normal Projection